Zone Contract Paradigms
# Considerations
- Data needed. State contains agent pose: x,y,z,θ,φ,ψ; cable angles: α,β.
- Zone definition
  - The safety zones contribute to the path constraints for the MPC controller(s) for inter-agent collision avoidance.
  - Extra constraints may be needed for payload trajectory
  - Are the zones static or dynamic?
  - Inter-agent collision avoidance: is zone crossover allowed?
  - Maneuvers permitted
  - Maneuvers prevented; viable areas that are excluded from the zones
- Modeling payload behavior
- Case study: how would it handle going over an obstacle?
# Centralized
Agent trajectories planned centrally to minimize sum of squared actuator effort, with full knowledge of agents’ states.
Safety zone definition:
- Safety radius centered on agent’s instantaneous pose. At each instant share agent poses and calculate a safety radius for each agent (0.5*min(r_n1,r_n2)-r_self).
  - Evolution over time: separation from other agents changes in time so radius must change over time. The central planner could predict the evolution of the safety radius by extrapolating from the agent’s current pose by the agent’s velocity over a fixed horizon.
  - The safety tubes are coupled functions of peer locations over time, so they will require significant computation.
  - Path constraints apply to the waypoints selected for each agent, so if the waypoint loci are not overlapping there will be no risk of collisions. The safety zones will not overlap at any instant.
  - Radially-symmetric safety radii cut out feasible space located away from peer agents.
- Cones of cable loci centered on agent’s attachment point. Each agent is given limits for the cable angles. If motion is constrained to the region of 3D space above the plane of attachment, then the pair of cable angles (α,β) defines a unique point in that region.
  - Would this permit configurations which lead to collisions? e.g. one at the front, two at the back symmetrically, the two back agents pull inwards sideways. Path constraints apply to the waypoints selected for each agent, so if the waypoint loci are not overlapping there will be no risk of collisions. The safety zones will not overlap at any instant.
  - Evolution over time: Separation between attachment points is fixed in time due to rigidity of body. The cones move with the payload in time. A central planner can estimate the payload trajectory given the agents’ trajectories. This estimate can be used to locate the attachment points and cones at any instant.
  - If the cable angle limits are static, there is less computation for the controller. Dynamic cable angle limits are unnecessary (extra path constraints due to environmental structure can be imposed)
  - Radially-symmetric cones cut out feasible space located away from peer agents.
Modeling payload behavior:
- An observer could estimate payload pose using the agents’ cable angle data. Using this estimate the controller could observe constraints on the payload dynamics.
- Distance tolerances for attachment points on the payload’s top surface can be considered when determining active constraints on the payload dynamics.
Case study: how would the scheme handle going over an obstacle?
Central controller implements obstacle height as a spatial path constraint using the estimate of the payload’s underside; all agents’ trajectories will observe this constraint.
# Distributed
Agent trajectories planned individually to minimize squared actuator effort, but agents communicate their state with peers.
Safety zone definition:
- Safety radius centered on agent’s instantaneous pose. At each instant agents share their poses and calculate their safety radius (0.5*min(r_n1,r_n2)-r_self).
  - Evolution over time: separation from other agents changes in time so radius must change over time. The agent could predict the evolution of the safety radius by extrapolating from peers’ poses by peers’ velocities over a fixed horizon.
  - The safety tubes are coupled functions of peer locations over time, so they will require significant computation.
  - Path constraints apply to the waypoints selected for each agent, so if the waypoint loci are not overlapping there will be no risk of collisions. The safety zones will not overlap at any instant.
  - Radially-symmetric safety radii cut out feasible space located away from peer agents.
- Cones of cable loci centered on agent’s attachment point. Each agent is given limits for the cable angles. If motion is constrained to the region of 3D space above the plane of attachment, then the pair of cable angles (α,β) defines a unique point in that region.
  - Would this permit configurations which lead to collisions? e.g. one at the front, two at the back symmetrically, the two back agents pull inwards sideways. Path constraints apply to the waypoints selected for each agent, so if the waypoint loci are not overlapping there will be no risk of collisions. The safety zones will not overlap at any instant.
  - Evolution over time: Separation between attachment points is fixed in time due to rigidity of body. The cones move with the payload in time.
  - If the cable angle limits are static, there is less computation for the controller. Dynamic cable angle limits are unnecessary (extra path constraints due to environmental structure can be imposed)
  - Radially-symmetric cones cut out feasible space located away from peer agents.
Modeling payload behavior:
- Using only its cable angles, the agent can estimate the position of the attachment points. Using peers’ and self cable angles, the agent can estimate the position of all attachment points and estimate the payload attitude.
- Using this estimate the controller could observe constraints on the payload dynamics.
- Distance tolerances for attachment points on the payload’s top surface can be considered when determining active constraints on the payload dynamics.
Case study: how would the scheme handle going over an obstacle?
At beginning of mission, implement the obstacle height as a spatial path constraint for each controller with respect to the estimate of the payload’s underside. All agents’ trajectories will observe this constraint.
# Decentralized
Agent trajectories planned individually; there is no communication with peers.
- Cannot implement safety radii without peer state communication.
- Cones of cable loci centered on agent’s attachment point. Each agent is given limits for the cable angles at the beginning. If motion is constrained to the region of 3D space above the plane of attachment, then the pair of cable angles (α,β) defines a unique point in that region.
  - Would this permit configurations which lead to collisions? e.g. one at the front, two at the back symmetrically, the two back agents pull inwards sideways. Path constraints apply to the waypoints selected for each agent, so if the waypoint loci are not overlapping there will be no risk of collisions. The safety zones will not overlap at any instant.
  - Evolution over time: Separation between attachment points is fixed in time due to rigidity of body. The cones move with the payload in time.
  - The cable angle limits must be static, so there is less computation for the controller. Dynamic cable angle limits are not possible due to lack of communication.
  - Radially-symmetric cones cut out feasible space located away from peer agents.
Modeling payload behavior:
- Using only its cable angles, the agent can estimate the position of the attachment points.
- No single agent has knowledge of more than one attachment point, so estimation of payload pose and dynamics is not possible. The agent is unable to observe constraints on the payload dynamics using this estimate.
- Distance tolerances for attachment points on the payload’s top surface are unknown.
Case study:
Must make assumptions about payload pose.